## Slide 1: Celestial-Inertial UAS Navigation in a GPS-negative Environment
Austin Kreulach
University of Arkansas
Department of Computer Science and
Computer Engineering
Harrison Welch
Austin Peay State University
Department of Computer Science and
Information Technology

## Slide 2: Presentation Structure
Importance of UASs
UAS Navigation
Non-GPS Navigation
Existing options
Celestial-Inertial Navigation
Notes: Contains: What exactly we plan to speak about

## Slide 3: Military Role of UASs
Surveillance
  Map making
  Enemy scouting
“Servicing the target”
  Elimination of threats
  Air support
Removing the human error from flying
  Save the life of the operator
  Improve operator efficiency
  Reduce weight from removing human-bearing equipment
  Operations limited by fuel, not sleep
Notes: Contains: What exactly we plan to speak about

## Slide 4: Entry into Civil Airspace
UASs growing cheaper
New requirement to ‘sense and avoid’
Demands location-sense and map-sense
https://sep.yimg.com/ay/yhst-17210252890263/aerosky-robosurfer-uav-glider-plane-4-channel-kit-2m-wingspan-3.jpg
Notes: Contains: What exactly we plan to speak about

## Slide 5: Why GPS is Objectively Excellent
http://www.gpsfortoday.com/wp-content/uploads/2009/09/spot-gps-tracking-device-coverage-map.jpg
Notes: Contains: What exactly we plan to speak about

## Slide 6: … but not perfect
GPS is incredibly easy to counter with a simple and cheap technology
The US is developing a system named NAVWAR aimed at disrupting enemy GPS signals.
VHF signals can interfere
Ionosphere disruption “scintillation”
Jamming, Spoofing, and Meaconing
Hill, Kashmir. "Jamming GPS Signals Is Illegal, Dangerous, Cheap, and Easy." Gizmodo. July 24, 2017. Accessed June 14, 2018. https://gizmodo.com/jamming-gps-signals-is-illegal-dangerous-cheap-and-e-1796778955.
“'Vulnerability Assessment of the Transportation Infrastructure Relying on the Global Positioning System,” tech. Rep., John A. Volpe National Transportation Systems Center, 2001. Accessed June 14, 2018. https://www.navcen.uscg.gov/pdf/vulnerability_assess_2001.pdf
"Federal Radionavigation Plan 1999," U.S. Department of Defense and U.S. Department of Transportation, December 1999. Accessed June 14, 2018. https://rosap.ntl.bts.gov/view/dot/8892/dot_8892_DS1.pdf?
Notes: Contains: What exactly we plan to speak about

## Slide 7: Alternatives to GPS Navigation
Inertial Navigation Systems
LiDAR
Infrasound
Signals of Opportunity
Optic Flow
Fingerprinting
Magnetometry
PALAD
Notes: Contains: What exactly we plan to speak about

## Slide 8
Use passive sensors to calculate the user’s position
Accelerometer drift problems
Zero Velocity Update (ZUPT) implementation
Less than 2% error in true location over a 15 minute walk
Ojeda, Lauro and Borenstein, Johann “Non-GPS navigation with the personal dead-reckoning system.” 2007. Accessed June 15, 2018. https://doi.org/10.1117/12.718691
Inertial Navigation Systems

## Slide 9: LiDAR Navigation
Used primarily for SLAM
Creates accurate depth maps using pulsed light
Pro: penetrative, precise
Con: active, expensive
R. Li, J. Liu, L. Zhang and Y. Hang, "LIDAR/MEMS IMU integrated navigation (SLAM) method for a small UAV in indoor environments," 2014 DGON Inertial Sensors and Systems (ISS), Karlsruhe, 2014, pp. 1-15.
Notes: Contains: What exactly we plan to speak about

## Slide 10: Infrasound Navigation
Low frequency sound able to travel long distances
Used by homing pigeons to home
Current experiments show promise but no current success
Pro: Would work everywhere Con: Doesn’t work anywhere
Bauer, Riley, Shannon Nolet, and Saad Biaz. "A Novel Approach to Non-GPS Navigation Using Infrasound." Brat Monthly, February 02, 1998, 0-1.

## Slide 11: Signals of Opportunity
Chunpeng Yan and H. Howard Fan, "Asynchronous differential TDOA for non-GPS navigation using signals of opportunity," 2008 IEEE International Conference on Acoustics, Speech and Signal Processing, Las Vegas, NV, 2008, pp. 5312-5315.
Signals of Opportunity Navigation

## Slide 12
Ultra High Accuracy Reference System (UHARS)
Large Antennas with 30 mile radius
LocataNet (contract developed a system of TimeLoc, keeping all the wide area synced to Nanosecond-accurate time
Known-point initialization to resolve ambiguous GPS references
Angelo Trunzo, 746th Test Squadron, USAF and John Amt, Locata Corporation ION GNSS 2011, Portland, Oregon, 23 September 2011
Network Triangulation

## Slide 13: Optical Flow
Optical Flow Navigation
Timizer, Selim, “Optical Flow Based Robot Navigation," 2001 Internal Publication, MIT
Notes: TODO: Find what to say here. Also the switch from Austin -> Harrison should occur either before this slide or immediately after it.

## Slide 14
Training Phase
  Implementations
    RSS
    Computer Vision
    Magnetometer
Comparison Phase
  “Position estimation”
  Many algorithm approaches
    WKNN or weighted k-nearest neighbor
    Neural Network
SENIL
  Extracts fingerprints from floor plans
Much work has been done to reduce the number of fingerprints size to then reduce its time to compare
Fingerprinting Navigation
X. Wang, J. Qiu, S. Ye and G. Dai, "An advanced fingerprint-based indoor localization scheme for WSNs," 2014 9th IEEE Conference on Industrial Electronics and Applications, Hangzhou, 2014, pp. 2164-2169.
doi: 10.1109/ICIEA.2014.6931530
Zain Bin Tariq, Dost Muhammad Cheema, Muhammad Zahir Kamran, and Ijaz Haider Naqvi. 2017. Non-GPS Positioning Systems: A Survey. ACM Comput. Surv. 50, 4, Article 57 (August 2017), 34 pages. DOI: https://doi.org/10.1145/3098207

## Slide 15
Use a preloaded magnetic anomaly map which was surveyed previously
  3 year old map
Constraint of having to fly at low altitudes
Reported 13m accuracy
Favorable conditions
High cost of sensors
  15,000 to 25,000
  optically-pumped scalar magnetometers
A. Canciani and J. Raquet, "Airborne Magnetic Anomaly Navigation," in IEEE Transactions on Aerospace and Electronic Systems, vol. 53, no. 1, pp. 67-80, Feb. 2017.
Magnetometry Navigation

## Slide 16
System of Determining in the attitude (directional angle) on a satellite
Use of a Panoramic Annular lens
  Reflect and refract light
  Full 360 degree view of the surroundings
Fairly large at 50 ft. diameter
Mark A. Stedham, Partha P. Banerjee “Panoramic annular lens attitude determination system (PALADS)” 1995. Accessed June 14, 2018. https://doi.org/10.1117/12.211498
Panoramic Annular Lens Attitude Determination

## Slide 17
Pro/Con of Prior Methods
 | Universality | Size | Cost | No Premap | Passive | UAV-Ready | Score
LiDAR | 0 | 1 | 1 | 1 | 0 | 1 | 4
Infrasound | 1 | 0 | 1 | 0 | 1 | 0 | 3
Signals | 0 | 0 | 0 | 0 | 1 | 1 | 4
Optical Flow | 1 | 1 | 0 | 0 | 1 | 1 | 4
Fingerprinting | 1 | 1 | 1 | 0 | 1 | 1 | 5
Magnetometry | 1 | 0 | 0 | 0 | 1 | 0 | 2
PALAD | 1 | 0 | 1 | 1 | 1 | 0 | 4
Astronav | 1 | 1 | 1 | 1 | 1 | 1 | 6

## Slide 18
Steps:
Take picture, and time
Identify stars
Determine relation between spheres
Relate star position and angle to current position
Celestial Navigation

## Slide 19
Gimbal
Camera Positioning
Mount

## Slide 20
Capture from Astrometry.net’s Gallery
Screenshot from Sellarium uploaded into nova.astrometry.net
The algorithm relies on prior knowledge of where the stars are in the sky
  Sloan Digital Sky Survey (yearly release)
Builds “quads” which are groupings of 4 stars
  2 most distant points forming an axis
  2 remaining star location about that axis are hashed and stored in a database
Bayesian decision of passing the is this a viable “quad”
Expectation of at least 1 million hashes for the entire night sky
Outputs out the RA and DEC of the input image
Dustin Lang, David W. Hogg, Keir Mierle, Michael Blanton, Sam Roweis. “Astrometry.net: Blind astrometric calibration of arbitrary astronomical images.” 2009. Accessed June 14, 2018. https://arxiv.org/pdf/0910.2233.pdf
We use Astrometry.net to analyze images of starfields to find named instance stars

## Slide 21
PyEphem is a Python library used to constrain the celestial sphere using absolute time

## Slide 22
Observer position can now be found using zenith imaging and celestial coordinates of instance stars

## Slide 23
Kalman Filtering
  Memory fading unscented
    Max error reduced by 21.4% and mean error reduced by 7.1%
  Matrices to filter sooth position estimations from raw data
Exponential Weighted Moving Average (EWMA)
Linearly Weighted Moving Average (LWMA)
  Less computationally complex
  Remove noise and human interference
X. Wang, J. Qiu, S. Ye and G. Dai, "An advanced fingerprint-based indoor localization scheme for WSNs," 2014 9th IEEE Conference on Industrial Electronics and Applications, Hangzhou, 2014, pp. 2164-2169.
doi: 10.1109/ICIEA.2014.6931530
F. Si, Y. Zhao and X. Zhang, "Memory fading unscented Kalman filter and its application in navigation by stellar refraction," 2017 IEEE Aerospace Conference, Big Sky, MT, 2017, pp. 1-8. Accessed Jun 15, 2018. http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=7943569&isnumber=7943554
Filtering

## Slide 24
Potential Points of Failure
https://stgreenie.wordpress.com/2014/10/05/star-stuck/
Magnification of error
Astrometry.net
  Runtime speed
  Accuracy
  Calculations
Day and twilight analysis
  Will there be enough stars
  Can this work in the daytime?
Photography quality
  Capture Speed
  ISO number,
  Aperture and focal length
Vehicular Attitude vs. Photography

## Slide 25
Importance of UAVs
UAV Navigation
Non-GPS Navigation
Available tools
Celestial-Inertial Navigation
Review